## Slide 1: The Intel new mexico Family & Friends amazing Car experience
Brought to you by NM Makers: Brian Baltz, Allison Barnes, David Manzanares, Todd Marsh, Dan Mcculley, Russ McInnis, Noel Paz, Janet Sholar, Alex Fei Event sponsored by Intel Global Brand & Reputation Marketing, Melissa Beers
Intel Maker Nation
presents
April 23rd 8:30am – 3:00pm
Notes: Give credit to IGB&RM and thanks to team for developing the event

## Slide 2: The Intel new mexico Family & Friends amazing Car experience
Thank you, if you have any questions please contact Allison Barnes or Todd Marsh
Inside Blue soco.intel.com/events/21970
Event introduces Intel® Arduino 101 to Intel employees, families & friends
build a car with coding & hardware experts available to answer questions
15 Teams will be randomly selected from the Inside Blue signup list
https://soco.intel.com/events/21970 An email notification will be sent if your Team is selected or placed on a waiting list
Saturday April 23rd from 8:30am to 3:00pm in RR7 TR1 & TR2
    Bring 2 family members/friends (3 people total per team 8yrs and older)
    ~4 hours for creating the Basic Car, ~2 hours for the smart and connected Intermediate and Advanced level cars
    Bring a laptop with a mouse and power cord
Beverages, Breakfast Snacks and Lunch will be provided

## Slide 3: Welcome
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience
Notes: Introduce Event Team
Building Layout
Cover Emergency Exits
Restrooms

## Slide 4: Today’s Agenda
8:30am – 8:45am
8:45am – 9:30am
9:30am – 11:30am
12:00pm – 12:30pm
12:30pm – 1:45pm
1:45pm – 3:00pm
Welcome
Intro to Arduino 101
Basic Module
Lunch
Intermediate Module
Advanced Module
Notes: Cover for NM the Device Depot Logistics with Kit
Cover Food/Snack Logistics
Cover Teams may leave at lunch

## Slide 5: Intro to Arduino 101
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 6: Arduino 101 Board
Arduino 101 & Genuino 101 are updated with the latest technologies. Featuring Intel’s Curie at their core.

## Slide 7: Arduino Terminology
IDE The Application you use to write code, and send it to the board and communicate with the board.
Sketch the “code” that you write and send to the board to control the I/O pins and anything connected to the board
Shield A printed circuit board/sensors that you connect to the board
Open Source A collective group that contributes to a topic…in this case Arduino and Galileo
Arduino besides being a Bar in Italy...it means “Strong Friend”
Notes: Let’s go over some terminology related to the Maker movement.

## Slide 8: Verify Arduino IDE and Intel Curie Board installed
Arduino IDE should be installed
  From - https://www.arduino.cc/en/Main/Software
  Intel Curie Boards should be installed
  In Arduino IDE Tools -> Board: -> Boards Manager -> Intel Curie Boards INSTALLED

## Slide 9: Connect Arduino 101 and Run Blink Sketch
Remove from the Tool Box the
  Arduino 101 and the USB cable
  Connect the USB cable to the PC and Arduino 101
Start Arduino IDE
  Click arduino.exe shortcut on desktop
Set Model
  In Arduino IDE
    Tools -> Board -> Arduino101
Set Port
  In Arduino IDE
    Tools -> Serial Port -> Port*

## Slide 10: Connect Arduino 101 and Run Blink Sketch (cont.)
With Arduino 101 connected and IDE open.
Start Blink sketch
File-> Examples -> 01. Basics -> Blink
Click Upload button ->
If the upload is successful, the console window will display “SUCCESS”.
  Repeat the process if you experience an error. If it fails again, check your Board and Port settings, USB connection and/or device driver.
Notes: Inform that that have to pick board and port
On upload tell them board will disconnect and reconnect from USB/PC
Ask users what happened?

## Slide 11: Basic Module
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 12: Time to Build our Racer...the Car
Take parts out of Tool Box
    Keep your placemat handy, it will help with part identification.
Order of Build:
    LEDs and cable
    Bottom Chassis
    Motors and Wheels
    LEDs and cable
    Batteries
    Bottom and Top Chassis
    Mainboard and Shield

## Slide 13: Addressable RGB LEDs and Cable
4x LED Mounts (N)
4x RGB LED(N)
1x LED Cable ()
Insert the RGB LED into the LED Mount
Install the LEDs into the cable connectors, so that the LONGEST lead is inserted into the Black box on the connector
  Do NOT put an LED into the connector on the short end of the cable
  NOTE: Fanning out the leads slightly make insertion into the connector easier
  The leads will not go entirely into the connector

## Slide 14: Test LEDs and cable assembly
LED Cable connection to Arduino 101
Insert a jumper wire into the black hole on the LED cable connector, connect the other end to one of the Arduino 101’s GND pin.
Insert a jumper wire into the hole next to the previously inserted wire. The 2 center holes of the connector will now have a wire. The other end of the jumper wire connects to the Arduino 101’s 5V pin.
Insert a third jumper wire next to the first wire you inserted into the cable connector. The jumper wire you just inserted should line up with the RED wire of the LED cable. Connect the other end of the jumper wire to the Arduino 101’s Digital 7 pin.
NOTE: There will be an open (unused) hole in the LED cable connector.

## Slide 15: Test LEDs and cable assembly (cont.)
With Arduino 101 connected and IDE open.
Start Racer LED Test sketch
File-> Sketchbook -> NMMakers_FnF_Event -> Examples ->LEDTest
    Upload the Sketch
All LEDs should light up, then
“Head lights,” “Brake lights,” and finally “Turn Signals.”

## Slide 16: Motors
4x LED Mounts (N)
4x RGB LED(N)
1x LED Cable ()
Insert the RGB LED into the LED Mount
Install the LEDs into the cable connectors, so that the LONGEST lead is inserted into the Black box on the connector
  Do NOT put an LED into the connector on the short end of the cable
  NOTE: Fanning out the leads slightly make insertion into the connector easier
  The leads will not go entirely into the connector

## Slide 17: Intermediate module
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 18: Advanced Module
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 19: Backup Material
Arduino 101 Quick Start
Intel Boards Quick Comparison
Amazing Car Experience
Parts Placemat
Connection Tables

## Slide 20: Arduino IDE and Curie Boards
Download and install IDE
  Go to https://www.arduino.cc/en/Main/Software and download the Arduino IDE for your OS. (Arduino 1.6.8 is the preferred version)
Install Arduino/Genuino 101 Core
  Double click on Arduino.exe shortcut
  In Arduino IDE, launch boards manager: Tools -> Board: -> Boards Manager
  Highlight Intel Curie Boards, and click Install
  You will be prompted multiple times to accept the driver/device software. Click Install for each prompt.

## Slide 21: Intel’s MicroComputer Comparison

## Slide 22: Arduino/Genuino 101 Specifications

## Slide 23: Intel’s Friends and Family: Amazing Car Experience Parts Placemat

## Slide 24: Intel’s Friends and Family: Amazing Car Experience Piezo Buzzer Connection Table
Piezo Buzzer:
Ardumoto Shield Pins | Jumper Wires
Digital 7 | Jumper Cable - (any color)
GND Header | Jumper Cable - (any color)

## Slide 25: Intel’s Friends and Family: Amazing Car Experience Motor and Motor Encoder Connection Tables
Ardumoto Shield Pins | Right Motor Jumper Wires
RIGHT MOTOR - B 3RED | Soldered on Motor Jumper Wire - BLACK
RIGHT MOTOR - B 4 BLACK | Soldered on Motor Jumper Wire - RED
Ardumoto Shield Pins | Left Motor Jumper Wires
LEFT MOTOR - A 2 RED | Soldered on Motor Jumper Wire - RED
LEFT MOTOR - A 1 BLACK | Soldered on Motor Jumper Wire - BLACK
Ardumoto Shield Pins | Left Wheel Encoder | Jumper Wires
Digital 2 | OUT (white) | Jumper Cable - (any color)
POWER Header | 5V (Red) | Jumper Cable - (any color)
GND Header | GND (Black) | Jumper Cable - (any color)
Ardumoto Shield Pins | Right Wheel Encoder | Jumper Wires
Digital 8 | OUT (white) | Jumper Cable - (any color)
POWER Header | 5V (Red) | Jumper Cable - (any color)
GND Header | GND (Black) | Jumper Cable - (any color)
Left Motor and Left Wheel Encoder:
Right Motor and Right Wheel Encoder:

## Slide 26: Intel’s Friends and Family: Amazing Car Experience Servo Motor and IR Proximity Sensor Connection Tables
Servo Motor:
IR Proximity Sensor:
Ardumoto Shield Pins | Servo Motor Cable | Jumper Wires
Digital 6 | Control Line | Jumper Cable - (any color)
POWER Header | 5V | Jumper Cable - (any color)
GND Header | GND | Jumper Cable - (any color)
Ardumoto Shield Pins | JST Cable from Sensor | Jumper Wires
Analog 0 | Data Line | Jumper Cable - (any color)
POWER Header | 5V | Jumper Cable - (any color)
GND Header | GND | Jumper Cable - (any color)

## Slide 27: Intel’s Friends and Family: Amazing Car Experience Piezo Buzzer Connection Table
LED Cable:
RGB LED leads:
Ardumoto Shield Pins | LED Cable | Jumper Wires
Digital 5 | Data Line (Red wire of LED Cable) | Jumper Cable - (any color)
POWER Header | 5V | Jumper Cable - (any color)
GND Header | GND (Black Marked wire of cable and connector) | Jumper Cable - (any color)
RGB LED leads | LED Cable Connector | LED Cable
Data out |  | Data Line (Red wire of LED Cable)
Ground Longest lead of LED | Indicated with Black box | GND (Black Marked wire of cable and connector)
V in |  | 5V
Data in |  | Data Line (Red wire of LED Cable)