## Slide 1: The Intel new mexico Family & Friends amazing Car experience
Brought to you by NM Makers: Brian Baltz, Allison Barnes, David Manzanares, Todd Marsh, Dan Mcculley, Russ McInnis, Noel Paz, Janet Sholar, Alex Fei Event sponsored by Intel Global Brand & Reputation Marketing, Melissa Beers
Intel Maker Nation
presents
April 23rd 8:30am – 3:00pm
Notes: Give credit to IGB&RM and thanks to team for developing the event

## Slide 2: Welcome
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience
Notes: Introduce Event Team
Building Layout
Cover Emergency Exits
Restrooms

## Slide 3: Today’s Agenda
8:30am – 8:45am
8:45am – 9:30am
9:30am – 11:30am
12:00pm – 12:30pm
12:30pm – 1:45pm
1:45pm – 3:00pm
Welcome
Intro to Arduino 101
Basic Module
Lunch
Intermediate Module
Advanced Module
Notes: Cover for NM the Device Depot Logistics with Kit
Cover Food/Snack Logistics
Cover Teams may leave at lunch

## Slide 4: Intro to Arduino 101
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 5: Arduino 101 Board
Arduino 101 & Genuino 101 are updated with the latest technologies. Featuring Intel’s Curie at their core.

## Slide 6: Arduino Terminology
IDE The Application you use to write code, and send it to the board and communicate with the board.
Sketch the “code” that you write and send to the board to control the I/O pins and anything connected to the board
Shield A printed circuit board/sensors that you connect to the board
Open Source A collective group that contributes to a topic…in this case Arduino and Galileo
Arduino besides being a Bar in Italy...it means “Strong Friend”
Notes: Let’s go over some terminology related to the Maker movement.

## Slide 7: Verify Arduino IDE and Intel Curie Board installed
Arduino IDE should be installed
  From - https://www.arduino.cc/en/Main/Software
  Intel Curie Boards should be installed
  In Arduino IDE Tools -> Board: -> Boards Manager -> Intel Curie Boards INSTALLED

## Slide 8: Connect Arduino 101 and Run Blink Sketch
Remove from the Tool Box the
  Arduino 101 and the USB cable
  Connect the USB cable to the PC and Arduino 101
Start Arduino IDE
  Click arduino.exe shortcut on desktop
Set Model
  In Arduino IDE
    Tools -> Board -> Arduino101
Set Port
  In Arduino IDE
    Tools -> Serial Port -> Port*

## Slide 9: Connect Arduino 101 and Run Blink Sketch (cont.)
With Arduino 101 connected and IDE open.
Start Blink sketch
File-> Examples -> 01. Basics -> Blink
Click Upload button ->
If the upload is successful, the console window will display “SUCCESS”.
  Repeat the process if you experience an error. If it fails again, check your Board and Port settings, USB connection and/or device driver.
Notes: Inform that that have to pick board and port
On upload tell them board will disconnect and reconnect from USB/PC
Ask users what happened?

## Slide 10: Basic Module
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 11: Time to Build our Racer...the Car
Take parts out of Tool Box
    Keep your placemat handy, it will help with part identification.
Order of Build:
    Bottom Chassis
    Encoders
    Motors and Wheels
    Side Struts
    Battery Holder and Batteries
    Completed Chassis
    Mainboard and Shield

## Slide 12: Encoders
1x Bottom Chassis Plate (A)
2x Encoder Mounts w/Encoders (E)
Attach Encoders to chassis
Snap the assembled encoder mounts into the back-left and right vertical slots of the Bottom Chassis Plate (A).
Note the Hall Effect Transistor will need to point to the outside edge of the chassis, and will need to oriented to the middle of the chassis.

## Slide 13: Motors and Mounts
2x Motors w/Encoder Magnets and Rear Mounts (D)
2x Front Motor Mounts (C)
Attach Motor Mounts
Slide a Front Motor Mount (C) onto the protruding eyelet on the front of a Motor (D). Ensure the rounded sides of the motor mounts are facing the same way.

## Slide 14: Motors and Mounts (cont.)
Attach the Motor Assemblies to the chassis
Snap the motor assemblies into the set of 2 horizontal slots of the Bottom Chassis Plate (A). Make sure that the rounded edges of the motor mounts and the wires are facing toward the center of the chassis
NOTE: Verify that the Hall Effect sensor is not rubbing against the Magnet (up to a 1/8" away) nor the motor shaft.

## Slide 15: Wheels
2x Wheel (U)
1x Nub Caster(F)
Attach the Wheels and Nub Caster
Slide a Wheel (U) onto the plastic shaft of a Motor (V). Notice the motor shaft has two flat edges. Make sure to line up the flat edges of the motor shaft with the flat edges of the wheel.
Snap the Nub Caster (F) into the slot on the back of the Bottom Chassis Plate assembly. Make sure the Nub Caster is on the side opposite the motors (the bottom side)

## Slide 16: Side Struts
Add the Side Struts
Snap the four Side Struts (H) into the diagonal slots on the four corners of the Bottom Chassis Plate assembly.
4x Side Strut (H)

## Slide 17: Battery Holder and Batteries
Install the 6 AA batteries into the holder. Use care to follow battery polarity.
Attach the battery cable to the holder.
Place battery assembly into Bottom Chassis plate
1x Battery Holder
1x Battery Cable
6x AA Batteries

## Slide 18: Mainboard Mounts
Attach the Mainboard Mounts
Snap the two Mainboard Mounts (G) into the vertical slots in the back of the top chassis plate near the large rectangular opening.
2x Mainboard Mount
1x Top Chassis Plate

## Slide 19: Complete the Chassis
Route the Cables
Position the Top Chassis Plate over the Bottom Chassis Plate – do not snap the two plates together yet. Make sure that the front sides of each plate line up. Mainboard Mounts to the back on top plate, nub caster to the back on bottom plate.
Route the wires and cables through the left and right oval slots in the Top Chassis Plate assembly as shown.
1x Bottom Chassis Assembly
1x Top Chassis Assembly

## Slide 20: Complete the Chassis (cont)
Attach Top Chassis Plate Assembly to Bottom Chassis Plate Assembly
Line up the Top Chassis Plate on top of all the struts, and carefully snap the Top Chassis Plate assembly onto the side struts and motor mounts. Press carefully and firmly above each side strut and motor mount until they each snap into place in the top chassis plate.
1x Bottom Chassis Assembly
1x Top Chassis Assembly

## Slide 21: Mainboard
Add the Mainboard
The Arduino 101 Mainboard (Z) snaps into the notches on the Mainboard Mounts (G) it will not be down to the lowest notch. Make sure the power jack is facing the left side of the robot (the Mainboard mounts should be closest to you). Push gently and evenly until it snaps into place.
NOTE: While applying downward pressure to the board, gently expand one of the mount legs, and repeat on the other until the mainboard is securely held in the Mainboard Mounts (the Mainboard should not move in the mounts).
1x Arduino 101

## Slide 22: Shield
Add the Shield
Attach the Ardumoto Shield to the Arduino 101.
Align all of the pins from the shield to the header of the Arduino 101 and gently press the shield onto the mainboard.
1x Ardumoto Shield

## Slide 23: Intermediate module
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 24: Time to add lights and sound to our Racer...the Car
Take parts out of Tool Box
    Keep your placemat handy, it will help with part identification.
Order of Build:
    RGB LEDs and cable
    Completed Chassis
    Piezo Buzzer

## Slide 25: Addressable RGB LEDs and Cable
4x LED Mounts (N)
4x RGB LED(N)
1x LED Cable ()
Insert the RGB LED into the LED Mount
Install the LEDs into the cable connectors, so that the LONGEST lead of the LED is inserted into the Black box on the cable connector.
  Do NOT put an LED into the connector on the short end of the cable
  NOTE: Fanning out the leads slightly make insertion into the connector easier
  The leads will not go entirely into the connector

## Slide 26: Test LEDs and cable assembly
LED Cable connection to Arduino 101
Insert a jumper wire into the black hole on the LED cable connector, connect the other end to one of the Arduino 101’s GND pin.
Insert a jumper wire into the hole next to the previously inserted wire. The 2 center holes of the connector will now have a wire. The other end of the jumper wire connects to the Arduino 101’s 5V pin.
Insert a third jumper wire next to the first wire you inserted into the cable connector. The jumper wire you just inserted should line up with the RED wire of the LED cable. Connect the other end of the jumper wire to the Arduino 101’s Digital 7 pin.
NOTE: There will be an open (unused) hole in the LED cable connector.

## Slide 27: Test LEDs and cable assembly (cont.)
With Arduino 101 connected and IDE open.
Start Racer LED Test sketch
File-> Sketchbook -> NMMakers_FnF_Event -> Examples ->LEDTest
    Upload the Sketch
All LEDs should light up, then
“Head lights,” “Brake lights,” and finally “Turn Signals.”

## Slide 28: Install LED cable w/LEDs and mounts into chassis
Route the LED cable into the chassis
Start with the short end of the cable in the center back of the chassis and route cable clockwise
Install the LEDs w/mounts into the Side Struts in the chassis corners
NOTE: The cable must not interfere with the encoders on the motors.
1x LED Cable with LEDs and Mounts

## Slide 29: Piezo Buzzer
Buzzer
Every robot should be able to make some sounds. Adding the buzzer will allow you to give your Racer a little personality with its own beeps and bops.
Add the Buzzer
Attach two jumper wires to the Buzzer, one wire will go to the GND header, the other to Digital pin 5.
1x Piezo Buzzer

## Slide 30: Advanced Module
Intel Maker Nation and NM Makers
Family and Friends Amazing Car Experience

## Slide 31: Time to add intelligence to our Racer...the Car
Take parts out of Tool Box
    Keep your placemat handy, it will help with part identification.
Order of Build:
    Top Chassis
    Servo Motor
    IR Proximity Sensor

## Slide 32: Servo Motor and mount
Install Servo Motor into Holder
Install Holder with Servo Motor into the Top chassis plate, rectangle in the front. Route the servo motor cable to the mainboard.
1x Servo Motor
1x Servo Motor Holder

## Slide 33: IR Proximity Sensor and Mount
Install IR Proximity Sensor into the Holder.
Attach the Cable to the sensor. Note the connector is keyed i.e. it only fits one way.
Attach the Holder with sensor and cable to the Servo.
1x IR Proximity Sensor
1x JST Cable
1x Proximity Holder

## Slide 34: Backup Material
Arduino 101 Quick Start
Intel Boards Quick Comparison
Amazing Car Experience
Parts Placemat
Connection Tables

## Slide 35: Arduino IDE and Curie Boards
Download and install IDE
  Go to https://www.arduino.cc/en/Main/Software and download the Arduino IDE for your OS. (Arduino 1.6.8 is the preferred version)
Install Arduino/Genuino 101 Core
  Double click on Arduino.exe shortcut
  In Arduino IDE, launch boards manager: Tools -> Board: -> Boards Manager
  Highlight Intel Curie Boards, and click Install
  You will be prompted multiple times to accept the driver/device software. Click Install for each prompt.

## Slide 36: Intel’s MicroComputer Comparison

## Slide 37: Arduino/Genuino 101 Specifications

## Slide 38: Intel’s Friends and Family: Amazing Car Experience Parts Placemat

## Slide 39: Intel’s Friends and Family: Amazing Car Experience Piezo Buzzer Connection Table
Piezo Buzzer:
Ardumoto Shield Pins | Jumper Wires
Digital 7 | Jumper Cable - (any color)
GND Header | Jumper Cable - (any color)

## Slide 40: Intel’s Friends and Family: Amazing Car Experience Motor and Motor Encoder Connection Tables
Ardumoto Shield Pins | Right Motor Jumper Wires
RIGHT MOTOR - B 3RED | Soldered on Motor Jumper Wire - BLACK
RIGHT MOTOR - B 4 BLACK | Soldered on Motor Jumper Wire - RED
Ardumoto Shield Pins | Left Motor Jumper Wires
LEFT MOTOR - A 2 RED | Soldered on Motor Jumper Wire - RED
LEFT MOTOR - A 1 BLACK | Soldered on Motor Jumper Wire - BLACK
Ardumoto Shield Pins | Left Wheel Encoder | Jumper Wires
Digital 2 | OUT (white) | Jumper Cable - (any color)
POWER Header | 5V (Red) | Jumper Cable - (any color)
GND Header | GND (Black) | Jumper Cable - (any color)
Ardumoto Shield Pins | Right Wheel Encoder | Jumper Wires
Digital 8 | OUT (white) | Jumper Cable - (any color)
POWER Header | 5V (Red) | Jumper Cable - (any color)
GND Header | GND (Black) | Jumper Cable - (any color)
Left Motor and Left Wheel Encoder:
Right Motor and Right Wheel Encoder:

## Slide 41: Intel’s Friends and Family: Amazing Car Experience Servo Motor and IR Proximity Sensor Connection Tables
Servo Motor:
IR Proximity Sensor:
Ardumoto Shield Pins | Servo Motor Cable | Jumper Wires
Digital 6 | Control Line | Jumper Cable - (any color)
POWER Header | 5V | Jumper Cable - (any color)
GND Header | GND | Jumper Cable - (any color)
Ardumoto Shield Pins | JST Cable from Sensor | Jumper Wires
Analog 0 | Data Line | Jumper Cable - (any color)
POWER Header | 5V | Jumper Cable - (any color)
GND Header | GND | Jumper Cable - (any color)

## Slide 42: Intel’s Friends and Family: Amazing Car Experience Piezo Buzzer Connection Table
LED Cable:
RGB LED leads:
Ardumoto Shield Pins | LED Cable | Jumper Wires
Digital 5 | Data Line (Red wire of LED Cable) | Jumper Cable - (any color)
POWER Header | 5V | Jumper Cable - (any color)
GND Header | GND (Black Marked wire of cable and connector) | Jumper Cable - (any color)
RGB LED leads | LED Cable Connector | LED Cable
Data out |  | Data Line (Red wire of LED Cable)
Ground Longest lead of LED | Indicated with Black box | GND (Black Marked wire of cable and connector)
V in |  | 5V
Data in |  | Data Line (Red wire of LED Cable)